2 Channel Mini DVR

Manual

Content

Keys on DVR……………………………………………………………………………………………….3

Side face on DVR……………………………………………………………………….…………………3

Icons on screen………………………………………………………………………..………………….4

How to connect with camera and monitor…………………………………………………..……….4

Switch camera to record…………………………………………………………………………………5

Set time and date…………………………………………………………………………….…………….5

Manual record setting………………………………………………………………….…………………6

Motion detection setting………………………………………………………………………………….7

Movie prerecord…………………………………………………………………………………………….7

File Overwrite Setting……………………………………………………………………….…………….7

Set motion detect range and sensitivity……………………………………………………………….7

Picture quality and TV mode setting ……………………………………………………………..……8

Resolution list………………………………………………………………………………………………9

Playback…………………………………………………………………………………………………..…9

6 Pictures preview mode……………………………………………………………………………..…10

Delete files…………………………………………………………………………………………………10

Read files by USB cable…………………………………………………………………………………11

Specifications…………………………………………………………………………………….……….13

Keys on DVR

| ↑ | Turn on motion detection |
| --- | --- |
| ↓ | Turn off motion detection |
| ← | Move left |
| → | Move right |
| OK/Menu | Confirm/enter into main menu |
| Power | Power indicator |
| Status | Working indicator |
| Playback | Playback videos |
| Switching | Switch cameras |
| Preview | 6 pictures preview |
| Rec. | Manual start/stop recording |

Side face on DVR

Icons on screen

How to connect with cameras

- 2 cameras can be connected with DVR and working at the same time

- Please take out the original 3 pins AV cable

- Yellow cable: one side connect with camera 1(video out) , and the other side connect with           DVR(V-in 1)

- White cable: one side connect with camera 2(video out) , and the other side connect with           DVR(V-in 2)

- Red cable: one side connect with camera 1 or camera 2(Audio out),the other side connect with DVR(Audio in)

(* The audio can be recorded when the camera have audio out function)

How to connect with Monitor/TV

- Please take out original 2 pins AV cable.

- Yellow cable: one side connect with DVR (video out) , and the other side connect with           monitor/TV (Video in)

- Red cable: one side connect with DVR (Audio out) , and the other side connect with           monitor/TV (Audio in)

Switch camera to record

You can see 2 different pictures on screen and choose which camera you need by press ”Switching” key in standby mode.

- If only 1 picture on full screen, the DVR only record 1 camera pictures, and the frame is 30f/s.

- When 2 pictures on screen, the larger picture is recording mode, the recording frame is 10f/s. The smaller picture is snapshot mode.

Set time and date

Insert a SD card before use it. Press “OK/Menu” key to enter into main menu and choose  icon.

- Choose Set Time/Date, press “OK” to confirm. Press”←, →”key to choose items. Press”↑,↓” to set.

- You can set the date format when you choose “YY/MM/DD”. Press”↑,↓” to set it.

Manual Record setting

1，Press ”OK” key enter into main menu and choose ,choose Master capture to set it.

2，Photo 1:Snapshot 1 photo when manual record

Photo 3: Snapshot 3 photos when manual record

Movie:  Record videos when manual record

Movie Clip: Record videos clips when manual record，10 seconds for every clip.

Motion detection settings

- Press “OK” key enter into main menu and choose icon.

Auto Capture: Choose ON to turn on motion detection, choose OFF to turn off.

- Mater Capture：4 working status under motion detection mode

Photo 1：Snap shot 1 photo when motion detected

Photo 3: Snap shot 3 photos when motion detected

Movie 5s: Record video for 5 seconds per clip when motion detected

Movie 10s: Record video for 10 seconds per clip when motion detected

- Movie Prerecord：

Choose ON to turn on prerecord function, choose OFF to turn off. This function will help DVR record videos between 2 clips. Generally speaking, 2-3 seconds can be saved in next clip.

- File Overwrite Setting:

Choose ON to turn on overwriting function, choose OFF to turn off. DVR will delete the 100MB to save new videos when SD card capacity less than 10MB.

Set motion detect range and sensitivity

- Press “OK” key enter into main menu and choose icon

Range：    You can choose 1/1（full screen）,1/4 screen,1/16 screen as surveillance area.

Timeslot：  You can choose 1,3,5 seconds as motion detect time

Sensitivity：Set motion detect sensitivity in Low, Middle, High status. The motion detection will be triggered easy when you set it high.

Picture quality and TV mode setting

1，Press ”OK” key enter into main menu and choose  icon

- Photo Quality (detail resolution please see the list below)

High quality: High resolution

Standard quality: Standard resolution

Low quality: Low resolution

- Movie Quality (detail resolution please see the list below)

QVGA: QVGA Resolution

D1:    D1 Resolution

Resolution in different status

| Status | Video | Snapshot |
| --- | --- | --- |
|  | 1 camera | 2 camera | 1 camera | 2 camera |
| D1&HIGH | 720x576 | 720x480 | 720x576 | 720x480 |
| D1&Standard | 720x576 | 720x480 | 720x576 | 720x480 |
| D1&Low | 720x576 | 720x480 | 720x576 | 720x480 |
| QVGA&HIGH | 360X288 | 360X288 | 720x576 | 360X288 |
| QVGA& Standard | 360X288 | 360X240 | 720x576 | 360X240 |
| QVGA& Low | 360X288 | 360X288 | 720x576 | 360X288 |

- TV Output Standard

You can choose PAL or NTSC mode to fit your Monitor and TV

Playback

Press “Playback” key in standby mode. You can see the video recorded time at the left corner. Press “←”“→” keys to choose the video you want to play back, and press “Rec.” key to play videos.

6 Pictures preview mode

Press “Preview” key under Playback mode.You can see 6 different pictures on screen, and you can press “←”“→” keys to choose the video by different timestamp at the left corner. Press “OK” to choose and press “Rec.” to play the video.

Delete files

- Press “Playback” key in standby mode. Press “OK” to Choose the file you want to delete, and then press “OK” to delete it.

File Delete: delete current file

Format: Delete all files in SD card（All files will lost and can not get them back.）

Read files by USB cable

- Connect DVR with computer by original USB cable.Turn on DVR, “MSDC” will display on screen

2, You can see the folder named “CCTV” in your computer.

- You can see many folders and named by different date.

For example：10032600.The format is Year/ Month/ Date.

- You can see many videos or pictures named by different time in the folder.

For example：133105-1. The format is Hour/ Minute/ Second

Specifications

| AV Input | 3 RCA ports (2 video+1 audio) |
| --- | --- |
| AV Output | 2 RCA ports (1 video+1 audio) |
| Frame | Pal:25f/s NTSC:25f/s |
| Resolution | D1:720X576 |
|  | QVGA:360X288 |
| Compression format | M-JEPG & Standard JPEG |
| Detect mode | Motion detection |
| Working mode | Recording/snapshot |
| Memory | SD/SDHC card≤32GB |
| USB port | USB 2.0 |
| Power | DC12V (5V-36V optional) |
| Working electricity | ≤250Ma |
| Working temperature | -10℃~+50℃ |
| Working humidity | 20%~85% |
| DVR weight | 160g |
| DVR dimension | 101X105X26mm (LxWxH) |

# Text boxes

|  | SD inserted |
| --- | --- |
|  | Manual start recording |
|  | Manual start snapshot |
| / | Record by motion detected |
| / | Motion detection status |
| 1 | Camera 1 video |
| 2 | Camera 2 video |
| 2010/03/31 | Date (Year/Month/Day) |
| 16:29:45 | Time（Hour/Minute/Second） |

| V-in 1 | Camera 1 video input |
| --- | --- |
| V-in 2 | Camera 2 video input |
| Audio in | Camera audio input |
| Audio out | Audio output |
| Video out | Video output |
| Power | Connect with power adapter |
| USB | Connect with original USB cable |
| Off/On | Power on/off |
| SD Card | Insert SD card |