JWC Group is set up since 1996 with area of S.M. 60000. We specializes in researching &developing hygienic products equipment, raw materials importing and exporting, hygienic products manufacturing and chemical products manufacturing. We are the top three manufacturer of hygienic products machinery in China with brand JWC.

More than sixty models of hygienic products machines (which are divided into eight series, they are diaper, sanitary napkin, panty liner, bed under pad, wet napkin, tissue napkin, packing, single use medical supplies) we design and manufacture fully meets the demand of our customers. Our production lines have been sold to more than 88 countries and areas. In the meantime, JWC trading company supplies different grades of raw materials for production and produce finished products of adult diapers.

JWC Group got ISO9001 and CE certificate and wins a lot of national and provincial reputation and awards.

For more information about us, please refer to SGS and BV report:

http://binsun.en.made-in-china.com/audited-supplier-reports/report.html

http://sinojwc.en.alibaba.com/trustpass_profile.html?ctype=detail&reportid=100015525

Welcome to our website：

www.sinojwc.com

公司部门掠影：

| Name | Full servo sanitary napkin bagger machine |
| --- | --- |
| Model | JWC-WZBJ |
| Equipment performance parameters |
| Power | 3 phases 380Vac，50Hz Cable sizes: 4×10mm2+1×6mm2 |
| Installation capacity | 16.5KW |
| Air source | _0.6MPa，gas source consumption≯200LPM |
| Designed speed | 70 bags /minute |
| Working speed | 60 bags /minute |
| Product specification | stacking type 10-30PCS， Inserting type 4-12PCS |
| Packing film type | Packaging film in roller |
| Packing film material | PE film or Complex film, The monolayer thickness ≤70µm |
| Packing film layout | Each page printed error ±1mm, containing at least 3mm×3mm color mark |
| Qualified rate | ≥99.9% |
| Overall size | L5.50m×W1.50m×H2.20m（L×W×H） |
| Equipment Color | silvery grey |
| Machine processing direction | According to customer’s request |
| Weight | About 3.5 ton |
| Price | standard configuration RMB 815000(include stacking unit) |
| Optional | Inkjet printer RMB 45,000 |

Full Servo Sanitary Napkin Bagger Machine

Model: JWC-WZBJ

1. Summary

1.1 Technical characteristics

1.1.1 Quick packing speed: stable speed is 60BPM

1.1.2 Full-auto packing: Feeding, bag-making, packaging –all processes are automatically

1.1.3 The product is highly adaptable: can simultaneously deal with inserting type and stacking type packing style without changing any mechanical structure, especially for stacking type short packets (such as pad)

1.1.4 It makes the time shorter of changing different size package because of the patented open-bag structure.

1.1.5 Patented open-size structure makes the production more stable.

1.1.6 High uniformity angle foled: patent angle folded structure makes higher uniformity.

1.1.7 Full servo driving way: 12-axis full servo driving system(including automatic arranging device), adopts absolute system-control which is easier to adjust the parameters.

1.2 machine parameters:

1.2.1 Overall max 3-dimentional size: L5.50m×W1.50m×H2.20

1.2.2 Main power: three-phase & five-wire 3Ph380Vac±10%、50Hz。

1.2.3 Air supply: air pressure_0.6MPa, total air consumption≯200LPM。

1.2.4 Electric capacity: installed capacity 16.5KW,load rate＜60%，cosö_0.8。

1.2.5 Running speed: design speed: 70BPM, stable working speed: 60BPM

1.3 Product type:

1.3.1 Full servo sanitary napkin (panty liner) final packing machine.

1.3.2 2 sides’ symmetry trust angle sealing way

1.3.3 Product specs: horizontal arranging out type: 10-30pcs, vertical arranging out type: 4-12pcs

1.4 Right Packing materials:

1.4.1 Packing products：Tri-fold sanitary napkin or panty liner (QQ package)

1.4.2 packing film：Roll bag packing film

1.4.3Packing film material: PE film or complex film, Single layer thickness≤70µm.

1.4.4Packing film printing layout: it has deviation for every printing layout _±1mm and has color code at least 3mm×3mm

1.4.5Packing film roll: inner diameter  Φ76.2mm（3 inches）,outer diameter maxΦ450mm.

1.5Function introduction

1.5.1Within the range of right material and products form, the machine stable working speed is 60BPM, working rate≥90%

1.5.2 Angle fold overlap≤3.5mm

1.5.3Angle fold Symmetry rate≤2mm

1.5.4 Sealing line parallelism, centrality ≤ 2mm

1.5.5Cutting lines parallelism ≤ 2mm. Bagging success rate of ≥ 99.9%.

1.5.6It can do many packing size and easy to change size at short time.

1.6 manufacturing process picture

1.7 machine structure

放卷伺服系统 unwinding servo system 制袋伺服系统 bag making servo system 套袋伺服系统 bagging servo system 人机交互系统 man-machine interactive system PLC控制系统 PLC control system 运动控制系统 motion control system 排链伺服系统托台伺服系统platform servo system 转盘伺服系统 turnplate servo system 张袋伺服系统 bag open servo system 推头伺服系统pusher servo system 后封伺服系统 back sealing servo system 出包伺服系统 bag output servo system

1.8 Parts Suppliers’ List

| Gear | BEM&NSK | Germany & Japan |
| --- | --- | --- |
| Motor | Siemens | Germany |
| Servo motor | Mitsubishi or Siemens(optional) | Japan or Germany |
| Reducer | VGM | Taiwan |
| Timing belt | Gates | USA |
| conveying belt | Habasit | Swiss |
| Sensor | OMRON /Banner | Japan /USA |
| Temperature controller | OMRON | Japan |
| Pneumatic element | SMC | Japan |
| Solenoid valve | SMC | Japan |
| PLC | Mitsubishi/Siemens | Japan/Germany |
| True color touchable screen | Mitsubishi/Siemens | Japan/Germany |
| Server | Mitsubishi/Siemens | Japan/Germany |
| Web guiding system | FIFE | USA |
| Electrical elements | Omron /Schneider | Japan/ France |
| Note: If the customer choose Siemens brand servo motor, Price increase 30% base on electrical parts cost |

Payment term:

1. Machine

30% T/T as deposit within 3 working days after contract signed, 30% T/T should be paid after buyers come to factory for machine supervising, and the rest 40% should be paid after buyer’s approved and supervised machine before shipping. The seller will deliver the machine within 3 days after receiving all payment.

  - Raw materials:

50% T/T as deposit, 50% T/T should be paid before shipping.

NOTE: train transportation fee and insurance are afforded by buyer.

Delivery time: 200 Days.

Supervise before shipping

Machine will be tested and supervised in seller’s factory before delivery. The time for testing in seller’s factory will not be more than 15 minutes. Raw materials consumption within 15 minutes will be afforded by seller. If customer needs prolong testing time, the extra cost will be afforded by customer.

Installation, testing, etc

- The Price of full set of machine includes machine price, spare parts, FOB Nanjing, salary and commissioning fees of our operators at buyer side. It’s better for buyer’s operator to have mechanical and electrical skills. We will be responsible for installation and training buyer’s workers.

2. Machine needs 2 operators, 4 packing workers. If there is a stacker, then 2 additional workers are required.

3. Factory area requirements: Length is 38meters, width is 10meters.

4. We will afford the salary of engineers for installation and testing machine for 21 days in buyer’s factory.

5. Our workers will stay mostly 21 days at buyer’s factory, among which 5 days are for installation and the other 16 days are for testing and training. If buyer still needs our workers to stay more time, then 50usd/person/day will be afforded by buyer. All fees needs to be paid before our workers leave buyer’s factory. Most importantly, they will stay there for at most 30 days.

6. Buyer will afford our workers’ accommodations and round air tickets cost.

7. Within the guarantee period, if there is emergency happened, we will assign our technical workers to repair and do the maintenance.

8. If urgent, seller will dispatch technician to buyer within the guaranteed period.

Important notes:

- The wastage excludes the circumstances when glue applicator breaks down or exchange material.

2. The latest time of residual payment or LC opening is 60 days after machine finished manufacturing. If buyer has not completed the payment or opened LC after 60 days, the Seller has the right to resell the machine and not return the deposit

3. Seller will inform Buyer come for supervising the machine in written paper sent by fax or by email.

4. Raw materials for production should be approved by JWC.

5. Buyer can’t privately ask our engineer stay at his factory work for them after our engineers finish the installation and training, if the buyer needs technician work with them for one year or longer time, the buyer has to contact our company manager. Otherwise, we have right to stop all the after sells service, and the Buy need to undertake all of our company loss.