### Key Programmer

### 1 AK400 Benz/BMW key prog

Keywords: benz bmw smart key maker, ak400, ak400key programmer, ak400 programmer, benz key programmer, bmw key programmer

Part No.: K016

Weight:  6.5KG

IR-Programmer(for Benz key)+Hitg2 programmer(for BMW key)+BEZN ESL

(election steering lock)K-Line programmer+912/9S12 in circuit programmer+68HC711 pragrammer+68HC705/05 programmer+68HC908 programmer+9CXX/95PXX/24CXX s-eprom programmer+BENZ key reader

+BMW key reader

Description:

All in one intelligence BENZ/BMW smart key maker

BENZ: W220/W208/W210/W220/W203/W215/W230/W209/W219/W211/W230/W215 (Big old key/Black key/Chrome key)

BMW: new 1/3/5/6/7 CAS/CAS2/CAS3/CAS3+system

1. Programming Benz smart key via infrared or on board programming, even the car lost all the key.

2. Read/Write BENZ ESL (election steering lock) via K-Line, no need take out ESL from the car.

3. Unlock BEZN ESL (election steering lock) via K-Ling with out key.

4. Read/Write BENZ ESL (key IG module)/BMW CAS/CAS2/CAS3 via ICP (no need take out MCU).

5. Renew smart key function, renew used Benz smart key.

6. Check status of Benz/BMW smart key before/after programmer

7.Renew Benz ME-ECU function.

8. Active ME2.0 ECU (4E28B), not need renew ECU

### 2. Mercedes-Benz key matching experts AK-500

KeyWords: ak500, ak 500 bmw key programmer, benz key programmer, key programmer, key programming, key transponder, ak500 key programmer

Part No.: K 018

AK 400 key programmer has been updated to latest products AK500 key programmer.

AK-500 is a carefully designed multi-purpose vehicle intelligent programming system that can adapt to a very good variety of programming environments. This product is a high degree of intelligence to realize the automatic programming function. AK-500 is a specialized vehicle to meet the modern high-level computer programming complex, high-efficiency and the development of a new generation of intelligent car computer programming system.

Support models:

-- Mercedes-Benz:W220/W220“Keyless Go”W208/W210/W220/W203/W215/W230/W209/W219/W211/W230/W215

-- BMW1/3/5/6/7/8/ MPC(MPC555/556,MPC561/562,MPC563/564),external Flash(MB58BW016,29BL802C,AM29BDD160,S29CD016,DE28F800 etc.) and external EEPROM(M95xxx)

-- Volkswagen Audi:MPC(MPC555/556,MPC561/562,MPC563/564),external Flash(MB58BW016,29BL802C,AM29BDD160,S29CD016,DE28F800 etc.) and external EEPROM(M95xxx)

### 3 Super Ad900 with 4D key clone king

KeyWords: ad900, super ad900key programmer, ad900 key programmer, super ad900 key programmer, auto key programmer, car key maker, auto key copier, auto key tool, auto key copy tool, auto repair tool

Part No.: K 027

The professional duplicating machine, Transpronics, has been designed and developed to assist immobilizer system specialists. Transpronics is not only a duplicating machine; it is also a unique machine that can make transponders from eeproms in immobilizer boxes when a customer has lost all keys. It can also inform you if a transponder is locked or not. It has been developed over 4 years. It can copy most crypto transponders like 42, 45,4D, most of 44 VAG and some 40 and 41 transponders. It can copy Texas fixed transponders to TPX1 without battery transponders.

- Identify Transponder
- Write Transponder Codes
- Copy Transponder
- Calculate eeprom memory
- Calculate Transponder Codes from eeprom memory
- Calculate pin-codes from eeprom memory , from chassis and from Transponder
- Test Transponder
- Generate Fixed Transponder Codes
- PC Software

Features:

1- Copy all fixed transponders
a- Temic 11
b- Temic 12
c- Megamos 13
d- Philips 33
e- Texas 4C

2- Copy most of crypto transponders
a- Philips Crypto 42
b- Philips Crypto 44 VAG
c- Philips Crypto 45
d- Texas Crypto 4D
e- Some Philips Crypto 40 and 41

3- Show all information about all transponders
a- Transponder Types
b- Transponder Codes
c- Locked or not
d- Which car brand
e- Eeprom codes
f- Pin-Codes

4- Calculate eeprom logics from transponder memory.
a- Temic 11 transponder (3 Bytes)
b- Temic 12 transponder (5 Bytes)
c- Megamos 13 transponder (4 Bytes)
d- Texas 4C transponder (4 Bytes)
e- Philips 33 Transponder (4 Bytes)

5- Calculate transponder logics from eeprom logics
a- BMW Philips 33 rolling Transponder
b- Opel Philips crypto 40 Transponder
c- VAG Philips crypto 42 Transponder
d- Vw Philips crypto 44 Transponder
e- Renault , Vw , Honda Rover, Opel, Alfa-Romeo Philips 33 Transponder
f- Fiat Palio - Siena Temic 11 Transponder
g- Mercedes Vito, sprinter, Vw Volt Temic 12 Transponder
h- Toyota 4C Transponder
i- Fiat Tipo- Tempra Megamos 13 Transponder
j- Fiat Second Generation Megamos 48 Transponder

6- Calculate pin-codes from transponders
a- Renault Philips 33 ( 4 Digits )
b- Peugeot Philips crypto 45 ( 4 Digits )

7- Calculate pin-codes from chassis numbers
Transpronics can calculate pin-codes for Hyundai and Kia from last 6 digits of chassis number.

8- Unlock most of 48 transponders.
As you know, new system cars lock the transponder during the programming. So you can not use these transponders again. But Transpronics can unlock most megamos crypto transponders with its high technology.

9- Generate Crypto Transponders from blank Crypto transponders for Renault，Chrysler and Jeep.
You can generate 46 Renault , Chrysler and Jeep transponders from blank 46 transponders.

10- Generate transponder logics for fixed transponders.

### 4.AD900 Key programmer

Keywords: ad900 key programmer, auto programmer, key programmer, ad900 car key programmer, car key programmer, key upgrade, ad900 key upgrade , car repair tool, AD900pro,

Part No.: K 023

Weight: 3.5KG

KEYWORDS: transponder duplicating system, transponder duplicating system manufacturer, transponder duplicating system supplier, pro transponder duplicating system, ad900 transponder duplicating system, original transponder duplicating system, transponder duplicating system

The professional duplicating machine, Transpronics, has been designed and developed to assist immobilizer system specialists. Transpronics is not only a duplicating machine; it is also a unique machine that can make transponders from eeproms in immobilizer boxes when a customer has lost all keys. It can also inform you if a transponder is locked or not. It has been developed over 4 years. It can copy most crypto transponders like 42, 45,4D, most of 44 VAG and some 40 and 41 transponders. It can copy Texas fixed transponders to TPX1 without battery transponders.

- Identify Transponder
- Write Transponder Codes
- Copy Transponder
- Calculate eeprom memory
- Calculate Transponder Codes from eeprom memory
- Calculate pin-codes from eeprom memory , from chassis and from Transponder
- Test Transponder
- Generate Fixed Transponder Codes
- PC Software

Festures:

1- Copy all fixed transponders
2- Copy most of crypto transponders
3- Show all information about all transponders
4- Calculate eeprom logics from transponder memory.
5- Calculate transponder logics from eeprom logics
6- Calculate pin-codes from transponders
7- Calculate pin-codes from chassis numbers
8- Unlock most of 48 transponders.
9- Generate Crypto Transponders from blank Crypto transponders for Renault，Chrysler and Jeep.
10- Generate transponder logics for fixed transponders.

### 5. SBB Key Programmer v31.02

KW: sbb key programmer, sbb, sbb key, sbb key pro, sbb key maker, mvp, t300, ad 900, ak400, auto key programmer, auto key maker, launch x431

Part No.: K015

Weight:  4KG

Latest version 03/2010.

SBB is a new device used as a portable unit for programming keys in immobilizer units on vehicles. Due to its integrated hardware SBB needs no more than the OBDII cable provided to carry out a wide range of functions.

Features:

--support update through Internet

--programming new keys
--reading keys from immobilizer's memory
--deactivating keys no longer in the car owner's possession
--operation by means of a menu guided programming
--programming new remote controls
--software with full database containing all the most important vehicle makes
--support multi Language

### 6. Zed-bull (Transponder clone) key programmer

Key word: zed bull key programmer, zed-bull, zed bull key prog, zed bull, key satkey cd

Part No.: K023

Zed-BULL is a transponder cloning device which contains all of Zed-Qxs features and also has more additional features. Zed-BULL will fulfill all of your requirements as professional on Immobilizer Systems.

Features:

- Transponder Cloning

- Finding PIN Code, preparing precoded transponders and programming transponders from EEPROM and MCU. For now, 55 different applications

- Producing Transponders for OBD Programming.

- Hitag2 Transponder Programmer

- USB communication and fast update

- Easy Use with Wide Graphic LCD Screen

- Surprise applications

### 7 AD90 key duplicator

KW: ad90 transponder key duplicator, ad90 key duplicator, ad90, ad900 key programmer, auto key programmer, car key programming, car key maker, car key programmer, auto scanner, car key duplictaor, auto maintenance, obd diagnostic tool

Part No.: K005

Weight:  1 KG

The professional duplicating machine, AD90, has been designed and built to keep peace with the constant evolution of transponder car keys.

The AD90 key duplicator features the most innovative electronic components in the field of radio frequencies thus allowing easy detection, reading and cloning (duplication) of fixed code transponders and the identification of cryptographic transponder codes.

The AD90 in addition has major features such as copying of Crypto 42 type transponders and the Texas 4C and 4D transponders.

These are additional options but make the AD90 a powerful tool.

### 8. Mercedes Benz Smart Key Programmer

KW: mercedes benz, benz smart, smart key, key tools, key programmers, smart remote, benz key tools, key makers

Part No.: K012

Weight:  2KG

This machine is use for new Benz Smart remote for Benz 220/215/210/202/203/219/211/231....

Description:

The new Mercedes device working with smart key (old and new) using in car since 1997 up to 2005 - without keyless go system. You can program new key (or used) in car and program old key if it do not work more. You read and program eeprom of CPU from Steering blocking module via diagnostic connector (38 pins). Desolder and read via programmer two CPU from Electronic Ignition Control Module. Load these eeproms to program. Desolder NEC CPU from the key. Soldering it on the device, select the No of key and program it. Solder all CPU on their

### 9 Toyota 4D + Smart Key Maker

KW: Toyota Lexus Smart Key, Toyota Smart Key maker, toyota key, smart key, remote, key programmer, diagnostic tools, key tools

Part No.: K004

Weight:  0.5 KG

--Support Toyota Lexus Smart Key

--Safe and efficient: Only need 20 seconds to add one key

--It is safe for the security alarm system

--Support all kinds of Toyota and Lexus smart key system: support K line and CAN-BUS protocols

--It is the most safe and fast key programmer device for Toyota and Lexus series till now.

--It supports all key lost

### 10 Mercedes benz OBD unlock ESL

KeyWords:mercedes-benz OBD unlock online esl, mercedes-benz, mercedes-benz e / c, mercedes-benz esl, unlock online esl

Part No.: K 020

Support Mercedes-Benz E / C series unlock online ESL, no need use other tools.

This product has the following characteristics: 

1; safe and efficient, ESL unlock only about 3 seconds; do not need to connect the computer; 

2; support for all Mercedes-Benz E / C series unlock ESL online; 

3; solve this model has been the control unit must be replaced ESL world problems, are only data communication through the OBD port unlock online ESL, a high degree of intelligence. Simple and easy to operate. 

4; the use of safety control unit will not damage ESL system; currently done at the same time Mercedes-Benz E / C Series ESL unlock the quickest, most secure equipment; 

5, this product has reached the level of intelligence the advanced international level, domestic technology leader. Maintenance of automotive electronics is also a fellow and the best car repair workshop equipment. 

Specific steps are as follows: 

1, the same truck and removed the plug ESL; plug unlock ESL instrument plug (no PC); 

2, to unlock ESL Miriam Benz OBD car diagnostic interface into OBD; 

3, OBD Mercedes-Benz Instrument ESL unlock about three seconds after the electricity, apparatus will "drop" is called 3 sound, alarm sound stopped; at this time to unlock the success of ESL;

### 11 MVP key decoder

KW: MVP key decoder, mvp key programmer, ad100, T300, T300 v5.98, T-code, ransponder key, key copy, repair, maintenance,

Part No.:K006

Weight:  4 KG

Covers all version functions (T300, AUTOMAM,K1,2005,2008,DECODER), and add more functions, such as the update 06-07 Honda system, Peugeot system and control, Hyundai system and control, the menu and control of Daewoo, Kia control, GM control and System update, Mitsubishi CAN BUS System, VW menu and control, CAN BUS Interface, etc.

### 12. T300 / t-code v9.2

Keywords: T300, T300 v7.2, T-code, transponder key, key copy, repair, maintenance

Part No.:  K003

Weight:  3.5 KG

When you lose all your car key (transponder key).You can program the new key by T300 .Also can program the remote control too. And read or count pin code.

It can be used to read out and erase fault code, read out the key open code, clear and copy key.

### 13 Honda FLY100 Scanner Locksmith Version

KeyWords:honda diagnostic system kit, honda diagnostic tool, fly100, honda fly100, honda fly108, fly100+gna600+ford vcm, auto diagnostic tool, auto repair, obdii scanner, obdii, car diagnostic tool, obd diagnostic tool

Part No.: K 017

FLY100 SCANNER LOCKSMITH VERSION IS the one-stop tool for HONDA all cars. It can do smart keys. No need to input password. The machine automatically calculate the password and enter the IMMO system.

### 14 4D key Clone King

KeyWords:4d key clone king, 4dkey clone king, 4d keyclone king, auto diagnostic tools

Part No.: K 022

Include one master machine , one double head line with 9 pin, one adapter and four DVD. This 4D key programmer machine connect with the computer, then immediate to clone 4D. Available for SILCA electron 4D and ours brand electron 4D.The Method is very easy and convenient. ( no need to get the password on internet )

Requirement of your computer:

Windows XP or windows2000 with a DVD Reader.

### 15 BMW Transponder Key Programmer

KeyWords:bmw transponder key programmer, bmw transponder key maker, bmw key maker, bmw key programmer, auto key programmer, auto key maker, auto parts, auto maintenance

Part No.: K 024

Support BMW Transponder Key ALL EWS AND CAS.

### 16 Mercedes Benz Key Maker

KeyWords:mb key prog, key programmer, auto diagnostic tools, benz key programming, benz key programmer, benz key maker, mercedes key programmer, mercedes benz key programmer, mercedes benz key maker, mb key programmer

Part No.: K 001

Program the key for Mercedes A-klasa, E210 ,ML320, W140, Gelenvagen with PCF7935 chip.

### 17 BMW key maker

KeyWords:bmw smart key maker, key programmer, smart key maker, bmw smart key pro, bmw smart key pro

Part No.: K 002

Features:

1. Programmer is for key programming PCF transponders 7930, 7931, 7935.

2. This programmer is very simple for using it and does not require additional equipment to work with EWS 2, 3, 3+.

3. The device is to erase the old and lost keys, add new keys on whatever position you want from 1 to 10 as you leave the existing keys working. You can program new keys when all keys are lost or stolen. The old keys will still work and you can order another key from the dealer beside the number of the new already programmed keys. To be able to program/add new key, you must use our special transponder made for the key programming

Note:

Programmer and adaptor BMW KEY MAKER are not used for 68HC11EA9 processor which has LOCK BIT on it.
If a processor has LOCK BIT on it, the program will warn about it.

### 18 Key Code Reader

KeyWords:auto key code reader, auto key programmer, key code reader, code reader, key programmer, auto key reader, key information reader, auto diagnostic tool, garage tools

Part No.: K 007

Introduction:

Reads fixed code transponders Philips®, Temic®, Megamos® (SILCA® 11, 12, 13, 21, 22, 23, 33, 40-45, 73), Texas® (SILCA® 4C, 4D) and writes PCF7930/31/35, TEMIC TK5550/1/4/7, T5.

KMRW-1T can copy TEXAS 4C transponders using KEYLINE TK23, TK24 transponder keys and SILCA electronic keys.

Recognizes crypto transponders MEGAMOS CRYPTO (SILCA® 48), PHILIPS CRYPTO2 (SILCA® 46) and TEXAS CRYPTO (SILCA® 4D).

Writes (it's not cloning function) PCF7936 in password mode, Megamos Crypto and TEXAS DST using PC. Possibility of software upgrade.

Read/write PCF7930/31/35, PCF7936 password mode, Megamos crypto, T5, TEXAS DST.

Support transponder:

TEMIC 1/32 ; TEMIC 1/40 ; MEGAMOS ; T5 ; PHILIPS PCF7930/31 ; PHILIPS PCF7935 ; PHILIPS PCF7936 ; MEGAMOS CRYPTO ; TEXAS ; TEXAS CRYPTO (DST) ; TEXAS CRYPTO 2 (DST+) ; PHILIPS PCF7930/31 ; MULTIPLY BLOCK

### 19 FORD(FOCUS), MAZDA Keymaker

KeyWords:ford(focus)mazda keymaker. ford(focus) keymaker, auto maintenance, auto repair, key programmer

Part No.: K 008

Introduction:

This item can support ford focus from year 2003 to 2007 and Mazda RX8 with TP01 and 60 of T1.The immobilizer module of Focus is located inside the instrument panel; it has no chip inside it, except Motorola 1K78X. The immobilizer module of RX8 is located near the ignition lock head, with chip 24C02 inside it.
This tool is easy to operate, no computer is needed. It uses a 9V battery; no external power connection is needed.

Operation Procedures

Focus Key Programmer: remove the cluster, connect the AK-60 to the BDM connector by using the connection cable, start AK-60, insert TP01 or 60 chip, press M2, When the LED flash for only one time, and the horn make only one sound, the key is copied successfully.

RX8 key programmer: remove the immobilizer module, de-solder the chip 240C2, clear each PINs, install it onto the adapter, then connect AK-60; turn on AK-60, insert TP60 or 60 chip, press M1 button. When the LED flash and the horn make a sound, the key is copied successfully.

Cautions!

When the LED flash for only one time, and the horn make only one sound, the key is copied successfully.

When LED flash for 5 times, and the horm make 5 sounds, there is connection problem between AK-60 and target chip.

When LED flash for 10 times, and the horm make 10 sounds, the TP01 or 60 chip model is not correct or it is locked

### 20 Fiat Key Programmer

KeyWords:fiat key programmer, fiat key pro, fiat key maker, ad 900, sbb, mvp, t300, ak-400, auto key programmer, auto key maker, bmw gt1bmw ops

Part No.: K 009

Support Fiat Siena, Palio, Weekend those models with Megamos encrypt ID48 chip ( work with 93LC66 of BSI computer) 
No need to connect computer and operate easily, 9V battery inside and no need to connect the supply power. 

Two functions of this programmer as follows: 
M1: Erasing all keys and programming new keys(press M1 3 times) when you lost all keys  
M2: Add new keys ( don?t need to remove the original keys)

The using method:

1 Remove BSI PC from the car, the BSI PC is in the left side of the driver, with the insurance seat for one seat.Need to remove the whole insurance box, and take out the BSI PC from the back of the insurance box,then weld 93LC66, the following picture for refence:     

2 After remove 93LC66?clear all the feet of 93LC66?insert 93LC66 to the adapter of this programmer as the following picture, then connect the adapter to the programmer.check below:  

3 Switch on?the LED turn red then trun green, which mean the programmer selt-test is normal.

4 Choose M1 or M2 to program keys?If the led light twinkle one time and the loudspeaker loud one tim, it shows that the programming is success.If LED lighting 5 times,and loudspeaker loud 5 times, it shows the wrong 93LC66 data or couldn?t find the 93LC66, need to check it is wrong with the connection or placement of the feet of 93LC66, and program keys again;If LED lighting 10 times, loudspeaker louding 10 times,it shows the ID48 chip is locked or the type of chip is wrong, need to program again.

5 Weld 93LC66 after finish the programming, and install BSI back to the car then it could be started.

### 21 Transponder cloning Tool

Keywords: keymam clone tool, transponder key tool, cloning tool, transponder key clone tools, transponder equipment

Part No.: K010

Weight:  2.5 KG

The best transponder programmer. Not like another programmer .When you check the transponder key .sometime is 4D ,Sometimes is 4C . The T Prog alway be true  !!!!

Features:

Read s fixed code transponders :

& PHILIPS PCF7930/3 1 -SILCA 33 , 73 ,

& PHILIPS PCF7935 40,41,42,44,4 5

& TEMIC -SILCA 1 1 i 12 ,

& MEGAMOS -SILCA 13 ,

& SILCA T5 ,

& TEXAS -SILCA 4C '

Recognises MEGAMOS CRYPTO -SILCA 48 , PHILIPS

CRYPT O -SILCA 46 , TEXAS CRYPTO 4D ;

Write s PCF7930/3 1 , T5-Nova and TEXAS 4C –

KEYLINE and SILCA ;

Fast detectin g th e existence o f transponder on a key ;Stan dalone tool ;Connect s t o a PC using usb interface -program Anahtar for Windows.

### 22 BMW HITAG-2 KEY (V3. 0)

KeyWords:new hitag 2 key programmer, hitag 2 key maker, hitag 2 key copier, new hitag 2key maker for bmw, hitag 2 key scan, hitag 2 key programmer, hitag 2 key for mbkey copy tool, new hitag 2 key maker, hitag 2 key code reader

Part No.: K 021

Functional Description:

1. support BMW (2002 -2009 years) CAS/CAS2/CAS3 DG512 / CAS3 + DP512. 

2. support matching BMW (2002 -2009 years) CAS/CAS2/CAS3 DG256 / CAS3 + DP512 key and remote control; the world's unique technology.

### 23 HITAG-2 Key Tool

KeyWords:hitag 2 key tool, hitag 2 key copier, hitag 2 key maker, hitag 2 key code reader, key maker, hitag 2 key repair tool, hitag 2 key key programmer

Part No.: K 013

With help of this tool you can generate key content for KEYS and transponders for Audi A8, VW Touareg, VW Phaeton, Bentley Continental, Porsche Cayenne, BMW E38, E39, E46, E53, E60, E61, E63, E64, E65, E66, E87, E90, E91, E92. Supported immobilizers EWS3, EWS3+, EWS4, CAS, CAS2, CAS3, Kessy, Kessy 2007/2008. With the help of programmer you can read and program internal key memory where are stored ODOMETER, VIN.

### 24 GAMBIT Transponder Key Maker

KeyWords:hitag gambit ii, key programmer, gambit ii, hitag2 key tool, hitag2key programmer

Part No.: K 014

GAMBIT Transponder KEY MAKER is intended for RFID ( transponders ) programming. It is mainly produced for programming RFID transponders and generating RFID transponders from the immobilizer dump/eeprom of the car, in order to be able to start the vehicle.

Gambit programmer works with PCF7935, PCF 7936 and T5 transponders which are not precoded and are completely blank.

### 25 BMW Key Reader

KeyWords:bmw key reader, bmw key programmer, key reader, bmw key, motocycle transponder, key programmer, key programming, benz key programmer

Part No.: K 011

When you drive your BMW to dealer's workshop for a service check, all you need to do is hand over your car key. All BMW models from the year 2000 or later store important vehicle information - the chassis number, mileage and the next due service date - on the key itself. Your BMW service partner accesses this using the electronic Key Reader. This system saves time and prevents errors, giving you and your BMW service partner more time to discuss your individual needs in greater detail.

Features:

It could identify 17 digit code for all new type of the car which were included E65 chassis, kilometer data at that time and all the info of the car's service. It could issue the service list soon since it has KSD man-hour system & ETK parts software.

Selling points:

1. Standard maintenance reception, solve the problem of abnormal maintenance.
2. Easy & quick, maintenance man needn't go in the car to check. He could spend more time to talk to customers which would increase customers' satisfactory degree.
3. Increase the reputation in customers.
4. Several languages are available.

Package including:

Key reader 1pc
Power adapter 1pc
CD(including KSD, drive & SAM disk) 1pc

### 26 HITAG-2 KEY (V3. 0) New

KeyWords:hitag-2 key programmer, hitag 2 key tool, hitag 2 key maker, hitag 2 key code reader, hitag 2 key key programmer, hitag 2 key repair tool

Part No.: K 029

New HITAG 2 key programmer is device programmer intended for programming of HITAG-2 transponders compatible with PHILIPS PCF7936 transponders. It can be used for reading/ programming of following type transponders:

*PCF7936 *PCF7941 *PCF7942 *PCF7944 *PCF7945 *PCF7946 *19732C202

Programmer supports both modes PASSWORD and CIPHER mode! Programming remote control pages. The Programmer can read and copy transponders known as Hi Tag 2, integrated in the new car models after 2003 year, all these transponders are in the keys of new vehicles like BMW, VW, Audi, Porsche, OPEL, SAAB, Peugeot, Citroen, Mitsubishi and so on . The programmer can work in password and cipher mode.

Functional Description:

1; support for BMW (2002 -2009 years) CAS/CAS2/CAS3 DG512 / CAS3 + DP512

2; support matching BMW (2002 -2009 years) CAS/CAS2/CAS3 DG256 / CAS3 + DP512 key and remote control; the worlds unique technology;

New functions:

With help of this tool you can generate key content for KEYS and transponders

--Audi A8, VW Touareg, VW Phaeton, Bentley Continental

--Porsche Cayenne

--BMW E60, E61, E63, E64, E65, E66, E87, E90, E91, E92.

Supported immobilizers EWS4, CAS, CAS2, CAS3, Kessy, Kessy 2007/2008

With the help of programmer you can read and program internal key memory where are stored ODOMETER, VIN, ...

Just need dump from your immobilizer, put your NEW KEY (or transponder) on programmer and generate working key!

### 27 PIN Reader for Chrysler

KeyWords:chrysler, pin reader, pin reader for chrysler, chrysler key, motocycle transponder, key programmer, key programming, benz key programmer, key reader, nec key programmer, nec programmer

Part No.: K 026

Pin Code reading device for Chrysler ( TYPE2)

Read data from Immobilizer controller and show the pin code on the screen of the device directly.

### 28 BMW Key Programmer (New)

KeyWords:bmw key programmer(new), bmw key prog, key programmer, new bmw key programmer

Part No.: K 019

This simple-designed programmer specially designed for BMW keys, is easy operating.

EWS2/3/3+, Rover75, MINI, Range Rover, Free Lander, Discovery. Ideal for lost or add keys

--Support on all the BMW with EWS, (including EWS2, EWS3 and EWS4).
--Only use normal chip can provide the efficaciously maintenance of broken keys of BMW.
--Read EWS Data via K line.
--This is a safe, credible produce and has own perennial maintenance.

### 29 Car key master (for Benz & BMW key)

KeyWords:bmw key program, mercedes benz key program, auto key programmer, ak500 key program, car key master, benz key programcar key programmer, benz key program for bmw, key programcar, key programmers, benz key program for benz, key programs

Part No.: K 030

Specialized in program key on BMW and Mercedes Benz now. VW AUDI 4generation IMMO is preparing.

Car key master, master the world. Both PC and handset models for your choice.

Multi-functions--- Integrate functions such as key information reading , data calculating, key writing , and is applicable to both old and new.

Easy operation--- Graphical workflow will make it easy for your operation. Whats more, our car key master can be operated via OBD socket, CAN K line on many models without disassembly.

High security G3 Platform--- Besides USB communication and online update, our G3(the third generation) platform is especially featured by its high security: hardware anti-cracking and software anti-copying, adopting IDEA (international Data Encryption Algorithm) for registration, upgrade and payment

Bran-new keys--- We will cooperate with German technology, and launch the bran-new keys for all the BMW and Mercedes Benz. At that time, you an get rid of the key shortage and no need to use any renovated second-hand keys.

Vehicle coverage:

Benz series:
Benz S CLASS ( W140, W220)
Benz CL CLASS (W215)
Benz SL CLASS ( R230)
Benz E CLASS (W210W211)
Benz CLK CLASS(W208W209)
Benz CLS CLASS(W219)
Benz C CLASS (W202W203)
Benz ML CLASS (W163)

BMW series:
Old style BMW(EWS2 EWS3 EWS4)
BMW 1/3/5/6/X (E87 E90 E91 E60 E61 E63 E70 E71) series white CAS2
BMW 1/3/5/6/X (E87 E90 E91 E92 E60 E61 E63 E64 E70 E71) series black CAS2
BMW 1/3/5/6/X (E87 E90 E91 E60 E61 E63 E64 E70 E71) series white CAS3
BMW 7 series E66 CAS 2005-CAS2

### 30 Yamaha bikes immobilizer emulator

KeyWords:yamaha bikes immobilizer emulator, immobilizer emulator, car scanner, obdii code reader, obdii eobdii, auto diagnostic tool, car diagnostic tool, auto scanner, auto repair, obdii scanner, obd diagnostic tool

Part No.: K 031

- The emulator of an immobilizer for motorcycles and scooters Yamaha.

- Works with all motorcycles and scooters Yamaha from 2006 to 2009.

- Does not need programming, only need to connect wires.

- Completely emulates work of a regular immobilizer, including light-emitting diode work on the instrument panel.

For emulator installation in the case of a regular immobilizer:

1. Remove glue hermetic from the immobilizer case. 
2. Take out a PCB from immobilizer and desolder from it wires. 
3. Connect the emulator according to drawing more low. 
4. Insert the emulator into the immobilizer case.  
 
Color of wires and their appointment:

Black (2 pcs.)  GND 
Red with a green strip  BATT (+12v) 
Red with a white strip  IGN (+12v) 
Blue LED (+5v) 
Yellow with a blue strip K-line Immo-ECU