SINO  INTERNATIONAL  SCAFFOLDING

Cuplock System Scaffold

All tubes of verticals and horizontals are high strength grade at 48.3x3.25mm. The topcups on verticals and blades on horizontals are made by drop forging. The tubes of Braces are also high strength grade at 48.3x2.3mm. And the bolts on braces are high strength grade. All items are at hot-dipped-galv. finishing, unless specified. Packing: in bundles. If using scrap steel material for packing, free of charge. But if using racks/basket, need to pay the cost of rack/basket. Loading: 20--22 tons/20' if used scrap steel material. 20--23 tons/40' if used racks/basket.

Cuplock Vertical Series Item Description Dim "A" (inch) Weight(kg) CV10 1 Cup Leg 0.5 Meter 1'-7-11/16" w/ s.spigot 1'-7-11/16" 3.47 CV33 2 Cup Leg 1.0 Meter 3'-3" w/ s.spigot 3'-3" 6.08 CV411 3 Cup Leg 1.5 Meter 4'-11" w/ s.spigot 4'-11" 8.58 CV66 4 Cup Leg 2.0 Meter 6'-62" w/ s.spigot 6'-6" 11.37 CV82 5 Cup Leg 2.5 Meter 8'-2" w/ s.spigot 8'-2" 13.80 CV910 6 Cup Leg 3.0 Meter 9'-10" w/ s.spigot 9'-10" 16.23 Cuplock Horizontal Series Item Description Dim "A" (inch) Weight(kg) CH110 1'-10-1/4"Horizontal 1'-10-1/4" 2.50 CH27 2'-7" Horizontal 2'7" 3.37 CH211 2'-11-7/16" Horizontal 2'-11-7/16" 3.75 CH30 3' Horizontal 3' 3.80 CH36 3'-6" Horizontal 3'-6" 4.38 CH40 4' Horizontal 4' 4.98 CH41 4'-1-1/4" Horizontal 4'-1-1/4" 5.10 CH411 4'-11-13/16" Horizontal 4'-11-13/16" 5.92 CH50 5' Horizontal 5' 6.00 CH511 5'-10-7/8" Horizontal 5'-10-7/8" 7.15 CH60 6' Horizontal 6' 7.30 CH70 7' Horizontal 7' 8.44 CH80 8' Horizontal 8' 9.60 CH82 8'-2-7/16" Horizontal 8'-2-7/16" 9.84 CH90 9' Horizontal 9' 10.75 CH100 10' Horizontal 10' 11.90 CupLock Caster Adapter Item Description CCA CupLock Caster Adapter

CupLock Swivel Clamp Brace Item Description Dim "L" (inch) Dim "A" (inch) Dim "B" (inch) CCB82 Swivel Clamp Brace 10'-6" 10'-6" 6'-6 3/4 " 8'-2" CCB80 Swivel Clamp Brace 10'-4-1/4" 10'-4-1/4" 6'-6 3/4 " 8'-0" CCB70 Swivel Clamp Brace 9'-7-1/8" 9'-7-1/8" 6'-6 3/4 " 7'-0" CCB50 Swivel Clamp Brace 6'-6" 6'-6" 6'-6 3/4 " 5'-0"

CupLock Swivel Face Brace Item Description Dim "L" (inch) Dim "A" (inch) Dim "B" (inch) CFB82 Swivel Face Brace 10'-6" 10'-6" 6'-6 3/4 " 8'-2" CFB80 Swivel Face Brace 10'-4-1/4" 10'-4-1/4" 6'-6 3/4 " 8'-0"

CupLock Board Bracket Series Item Dim "L" (inch) Number of Boards CCB110 1'-10-1/4" 2 Board CBB27 2'-7-5/16" 3 Board

CupLock Steel Ladder Bracket Item Description CLBW Steel Ladder Bracket

Steel Ladder Series Item Description Dim "L" (inch) CSLW3 Steel Ladder 3' 3' CSLW5 Steel Ladder 5' 5' CSLW10 Steel Ladder 10' 10'

CupLock Screw Jack Item Description Weight(kg) SJB Screw Jack 3.5

CupLockSwivel Screw Jack Item Description Weight(kg) SJS Swivel Screw Jack 3.8

CupLock Caster Item Description Weight(kg) SCU-12 12" X 3" Scaffold Caster 3.8

CupLock Scaffold Stair Unit (Left/Right) Item Description Dim "L" (inch) Weight(kg) CSSL/R82 Scaffold Stair Unit (Left or Right) 8'-2' 32 CSSL/R80 Scaffold Stair Unit (Left or Right) 8' 30

CupLock Scaffold Stair Tread Item Description Dim "L" (inch) Weight(kg) CST36 CupLock Stair Tread 3'-6" 3'-6' 7.03 CST40 CupLock Stair Tread 4'-0" 4'-0' 8.0

Scaffold Rack Standard-Grey Painted Item Description Weight(kg) SRS Scaffold Rack Standard –Grey Painted 46

Scaffold Basket Rack with Nets-Grey Painted Item Description Weight(kg) SBRN Scaffold Basket Rack with Nets-Grey Painted 75

Frame System Scaffold

F06L Series (Powder Coating) Item Description Width Weight(kg) SI1524 Walk Thru Frames 16Mn 1524 20.6 SI1219 Walk Thru Frames 16Mn 1219 19.3 SI1067 Walk Thru Frames 16Mn 1067 18.7 SI914 Walk Thru Frames 16Mn 914 18.1 FM Series (Powder Coating) Item Description Width Height Weight(kg) TJJ5 Mason Frame 16Mn 1524 1524 16.9 TJJ6 Mason Frame 16Mn 1524 1219 15.2 TJJ4 Mason Frame 16Mn 1524 1930 21 FM3 Series (Powder Coating) Item Description Width Height Weight(kg) TJJ3 Mason Frame 16Mn 1219 914 13.4 TJJ33 Mason Frame 16Mn 4914 914 11.3

Shoring Frame (Powder Coating) Item Description Dim "A" (inch) Dim "B" (inch) SF23 2'X 3' Shoring Frame 2' 3' SF24 2'X 4' Shoring Frame 2' 4' SF25 2'X 5' Shoring Frame 2' 5' SF26 2'X 6' Shoring Frame 2' 6' SF43 4'X 3' Shoring Frame 4' 3' SF44 4'X 4' Shoring Frame 4' 4' SF45 4'X 5' Shoring Frame 4' 5' SF46 4'X 6' Shoring Frame 4' 6'

Snap-On Frame (Powder Coating) Item Description Dim "A" (inch) Dim "B" (inch) F388 3'X 8'-8" Snap-On Frame 3' 8'-8" F3108 3'X 10'-8" Snap-On Frame 3' 10'-8"

Shoring Frame (Powder Coating) Item Description Dim "A" (inch) Dim "B" (inch) F368L 3'X 6'-8" Snap-On with Ladder 3' 6'-8" F3108L 3'X 10'-8" Snap-On with Ladder 3' 10'-8"

Snap-on Box (Powder Coating) Item Description Dim "A" (inch) Dim "B" (inch) F220 2'X 20' Snap-On Box 2' 20' F240 2'X 40' Snap-On Box 2' 40' F320 3'X 20' Snap-On Box 3' 20' F340 3'X 40' Snap-On Box 3' 40' F520 5'X 20' Snap-On Box 5' 20' F540 5'X 40' Snap-On Box 5' 40' F34 3'X 4' Snap-On Box 3' 4'

Snap-on DoubleBox (Powder Coating) Item Description Dim "A" (inch) Dim "B" (inch) F55 5'X 5'-1" Snap-On Double Box 5' 5'-1" F568 5'X 6'-8" Snap-On Double Box 5' 6'-8"

B-CrossBrace Item Description Weight(kg) XC2502 7'X 4' Tube Brace 4.8 XC3327 1'X 10' Tube Brace 7.3

Guard Rail Item Description Dim "A" (inch) GR3 3'Guard Rail 3' GR42 3'-6"Guard Rail 3'-6" GR4 4'Guard Rail 4' GR5 5'Guard Rail 5' GR7 7'Guard Rail 7' GR10 10'Guard Rail 10'

Frame Parts Item Description Weight(kg) LG1117 Comer Rail Post Female Pwd Coat 3.6 LG1305 Comer Rail Post Male Pwd Coat 3.8

Frame Parts Item Description Weight(kg) LJJ Coupling Pins HDG+Spring RivetEG Q235 0.5

Frame Parts Item Description SAU3 3' Access Ladder Powder Coating SAU6 3' Access Ladder Powder Coating

Frame Parts Item Description Weight(kg) DL Ladder Bracket-PWD Q235 3

Frame Parts Item Description Weight(kg) SJJ 20'SIDE BRACKETS Q235 5.2

Ringlock System Scaffold

All tubes of Verticals & Horizontals are high strength grade at size 48.3x3.25mm. The ring plates are at 10mm thickness. The ends on the Horizontals are casting steel. All tubes of Braces are high strength grade at size 48.3x2.3mm. And the bolts are high strength grade. All items are at hot-dipped-galv. finishing, unless specified. Packing: in bundles. If using scrap steel material for packing, free of charge. But if using racks/basket, need to pay the cost of rack/basket. Loading: 15--22 tons/20' if used scrap steel material. 16--23 tons/40' if used racks/basket.

RingLock Vertical Series Item Description Dim "L" (cm) Weight(kg) RV010 Stand 050 with Spigot 50 3.5 RV-033 Stand 100 with Spigot 100 6.0 RV-0411 Stand 150 with Spigot 150 8.5 RV-066 Stand 200 with Spigot 200 11.0 RV-082 Stand 250 with Spigot 250 13.5 RV-091 Stand 300 with Spigot 300 16.0 RV-131 Stand 400 with Spigot 400 21.0 RV-010SPL Item Description Weight(kg) RV-010SPL Start Standard 66 4.5 RingLock Base Collar Item Description Weight(kg) RBC Base Collar 1.7

RingLock Vertical without Spigot Series Item Description Dim "L" (cm) Weight(kg) RV-0411-WS Standard 150 W/o Spigot 150 7.7 RV-066-WS Standard 200 W/o Spigot 200 10.2 RV-082-WS Standard 250 W/o Spigot 250 12.7

RingLock Horizontal Item Description Dim "L" (cm) Weight(kg) RH040 Ledger 40 40 2.4 RH050 Ledger 50 50 2.8 RH070 Ledger 70 70 3.7 RH075 Ledger 75 75 5.1 RH100 Ledger 100 100 4.7 RH150 Ledger 150 150 7.2 RH200 Ledger 200 200 8.9 RH250 Ledger 250 250 11.0 RH300 Ledger 300 300 13.0

RingLock Lattice Girder Item Description Dim "L" (cm) Weight(kg) RLG400 Lattice Girder 4.00 Meter 400 50.5

RingLock Double Ledger Item Description Dim "L" (cm) Weight(kg) RDL150 Double Ledger150 150 12.8 RDL200 Double Ledger200 200 17.0 RDL250 Double Ledger250 250 20.7 RDL300 Double Ledger300 300 23.6

RingLock Wing Maintenance Beam Item Description Dim "L" (cm) Weight(kg) WMB200 Wing Maintenance Beam 200 21.6 WMB400 Wing Maintenance Beam 400 39.0

RingLock Bay Brace Item Description Dim "A" (cm) Dim "B" (cm) Weight(kg) RBVD100 Diagonal 100X200 200 100 8.6 RBVD110 Diagonal 110X200 200 110 8.7 RBVD150 Diagonal 150X200 200 150 9.3 RBVD200 Diagonal 200X200 200 200 10.2 RBVD250 Diagonal 250X200 200 250 11.3 RBVD200X150 Diagonal 200X150 150 200 9.2 RBVD110X150 Diagonal 110X150 150 110 7.4 RBVD250X150 Diagonal 250X150 150 250 10.4 RBVD300 Diagonal 200X300 200 300 12.8

RingLock Board Bracket Item Description Weight(kg) RBB70 Side Bracket 2 Board 6.5 RBB40 Side Bracket 1 Board 5.0

U-Head Screw Jack Item Description Weight(kg) SJB-U U-Head Screw Jack 6.3

RingLock Screw Jack Item Description Weight(kg) SJB Screw Jack 3.5

RingLock Swivel Screw Jack Item Description Weight(kg) SJS Swivel Screw Jack 3.8

Scaffold Rack Standard-Grey Painted Item Description Weight(kg) SRS Scaffold Rack Standard –Grey Painted 46

Scaffold Basket Rack with Nets-Grey Painted Item Description Weight(kg) SBRN Scaffold Basket Rack with Nets-Grey Painted 75

Quicklock System Scaffold

Quick Lock Vertical Series Item Description Dim "L" (cm) Weight(kg) QL100 Quick Lock Vertical 100 100 6.2 QL200 Quick Lock Vertical 200 200 11.7 QL250 Quick Lock Vertical 250 250 14.4 QL300 Quick Lock Vertical 300 300 17.2 Quick Lock Ledger Series Item Description Dim "L" (cm) Weight(kg) QL120 Quick Lock Ledger 120 120 5.55 QL180 Quick Lock Ledger 180 180 6.95 QL240 Quick Lock Ledger 240 240 8.85 Quick Lock Transom Series Item Description Dim "L" (cm) Weight(kg) QL80 Quick Lock Transom 080 80 5.9 QL120 Quick Lock Transom 120 120 9.7 QL180 Quick Lock Transom 180 180 13.10

Quick Lock Face Brace Item Description Dim "L" (cm) Weight(kg) QFB41 Quick Lock Face Brace 080 274 10.9 QFB42 Quick Lock Face Brace 080 354 13.1

Quick Lock Board Bracket Item Description No.of Board Weight(kg) QBB51 Quick Lock Board Bracket 1 2.34 QBB52 Quick Lock Board Bracket 2 5.82 QBB53 Quick Lock Board Bracket 3 9.54

Quick Lock Tie Bar Item Description Dim "L" (cm) Weight(kg) QTB1 Quick Lock Tie Bar 1.245 Meter 1.245 3.52 QTB2 Quick Lock Tie Bar 1.803 Meter 1.803 5.20 QTB3 Quick Lock Tie Bar 2.413 Meter 2.413 7.00

Indoor System Scaffold

Accessories for scaffolds

Formworks Props /Postshorings Clamps/Couplers for scaffolds Wheels/Casters for scaffold Other Fittings/Accessories for scaffolds Other Fittings/Accessories for scaffolds Other Fittings/Accessories for scaffolds