NPP-688-C

Transparent Rubber Paste

NPP-688-C is the transparent paste for printing usage which is mainly applied for general fabrics (Cotton, Polyester, Nylon,…etc.).

Character

- Non-tacky, soft-feel

- High glossy surface

- Excellent color sharpness and elasticity

- Less migration impacts to disperse dyestuff on substrate

- Excellent washing fastness

Application

Due to long term storage, water might be separated and drifted over the surface. This is normal condition without any harm to quality, please just stir well before use. Viscosity Adjustment: Mix up with a bit of water for viscosity reduction if necessary. Since it can be scraped easily, water is basically not suggested to be added as the high viscosity paste would not be penetrated into the fabric easily and then obtain excellent glossy effect and soft feel. Addition of Pigment: The pigments can be directly added into the paste and then stir well for use and water is allowed to be added to adjust viscosity if necessary. Drying rate is subject to the pigments and the dosage.

Specification

- Appearance			：Transparent Paste.

- Main Ingredients	：Macromolecular Polymer, Water

- PH  Value			：7 ~9

- Package				：Net Weight 50KG / Blue PE Drum &

30KG / Blue PE Drum

- Safety				：Avoid the direct touch of skin and eyes.

- Storage				：Keep container airtight and away from fire. Store

it in a cool(10°C~40°C), dark, and ventilated place.

Memo

All recommendations are given only for reference; we do not guarantee the results of operation of which we have no direct control.  For further request, please contact to our technician for best solution.