NPP-688-CKW

Chapping White Paste

NPP-688-CKW is a white paste for printing, and developed to create irregular cracked texture on surface after curing.  It is not only easy to operate but also a good paste to produce elastic, soft hand-touch and solid washing fastness products.

Character

- Create irregular cracked texture on surface after dried

- Flexible to control the width of crack-line.

Application

NPP-688-C transparent rubber paste mixed with NPP-688-W white rubber paste and BCA-3070 Bottoming Additive 1% to bottom the basis twice. Mix up NPP-688-CKC with NPP-688-CKW by 50~70% and 30~50%, respectively to print. Printing operation can be performed after slightly dried for the next layer. The more percentage of NPP-688-CKC applied the more strength of downward- binding gained. Mixing with PRC series is highly recommended to produce accurate and bright colors. Suitable for screen with less 120 mesh.

Specification

- Appearance			：White Paste.

- Main Ingredients		：Macromolecular Polymer, Water, TI02.

- PH  Value				：8±1

- Package				：Net Weight 50KG / PE Drum.

- Safety					：Avoid the direct touch of skin and eyes.

- Storage					：Keep container airtight and away from fire.

Store it in a cool(10°C~40°C), dark, and ventilated

place.

Memo

All recommendations are given only for reference; we do not guarantee the results of operation of which we have no direct control.  For further request, please contact to our technician for best solution.