1. Introduction	1

2. Installation	1

2-1 Driver installation for Skin Camera (USB 225)	1

2-2 free installation the Driver of hard lock (Softdog)	3

2-3 Skin Master installations	3

3-1 Option	5

4. Backup and restore	7

4-1 Backup	7

4-2 Restore	8

5. Registration Search	8

5-1 Customer information	8

5-2 Non-Member Measure	10

6. Main Manu	10

6-1 Moisture	10

6-2 Sebum	11

6-3 Pore	13

6-4 Keratin	14

6-5 Surface	15

6-6 Pigmentation	15

7. Client report	16

7-1 products	17

7-2 Printout report	17

8. FQA	18

8-1 How do you know the installation of USB camera is normal?	18

8-2 The images does not appear on the screen, how to fix?	18

# 1. Introduction

The Skin master is intelligent skin diagnosis software with six functions. The Skin master will be available to support most of skin USB cameras on the market (VGA≥640x480 only!). The six analysis modules can be accurately detected skin moisture, sebum, pore, wrinkle, surface, keratin and pigment changes in the situation. It will be surprising the skin can be replay by similar 3D image, and you can turn the 3D skin and observation by the different angles. The client report not only can be printout the beauty result for client, and also it can be according to diagnosis results to match suitable products automatically.

# 2. Installation

### 2-1 Driver installation for Skin Camera (USB 225)

- Insert the utility CD into the CD-ROM driver, the software installation menu will appear automatically.

- If the software installation menu does not automatically display, open windows explorer and double-click the “autorun.exe” icon in the CD-ROM directory.

- When installation starts, a list of application software will be shown. You can either-

-   Click on the “next” box in the front of each software or select, or

- Click on the “continue” botton

Recommendation on installing software for specific purposes.

Note: software are re-installable. If you did not install specific software during installation, you can re-do the installation to install them at any time.

- Then click install button so start. Follow the instruction to finish.

- “The installation may need to reboot your system. Please save all open documents before you start”.

Please plug-in USB-Camera to USB port and computer will be recognize the camera soon and you will be find “Dual Mode USB Camera OV519 #3”at “Device manager”

### 2-2 free installation the Driver of hard lock (Softdog)

Skin master was used the new hard lock to replace old softdog since June 15, 2007. You do not need to installation the hard lock driver because it is available for any version of Windows XP.

### 2-3 Skin Master installations

Double click                       ( the software will be installed

automatically.

3. Before enter the software

Double click the shortcut icon on the desk and enter the start Manu of software, see as blow:

If you are the first to enter the software, suggest you first understand and fulfill the “option” and "Product Registration" and then enter the software.

### 3-1 Option

Double click “Option” of Start menu and enter “Option”, as shown in the following figure.

There are five modules on the Option: Pore Test Setting; PassWord; DataBase; Advice; and Logo.

3-1-1 Pore Test Setting

To better show the effect of draw, we can set up different colors for the test results, see the as below:

3-1-2 Password

You can set up different password for different operators. The setting way: Select  ( Input Existing PW(Input New PW(PW confirm(save. You can use the new PW to enter software after set up new PW.

3-1-3 Database

To list point the box of the Backup period(input three digit(Click “restore”

3-1-4 Advice

You can pre-input some recommendations for printout report, but also you do nothing and input some suggestions on the report directly.

3-1-5 Logo

Click “Logo”( Select the image file (BMP only!)(OK.

The logo will be display the upper left corner of the report automatically.

3-2 Product Register

Click “Product Register” and enter the new manu as below:

First, Click “Register” on the bottom right corner(Click “Open” on the upper left corner, select the picture of product (Click “Advertising” and the product picture will be demo on the main manu.(Input information to “Class”; “Model”; “Product” and “Price”(Select and point one of “Skin type” (Select and point one or all the Pore, Keratin, Surface Pigment or Worst, Bad, Normal, Good and Best (the selected products will be matched the result of test after Click “product” on the printout report automatically.(Click “Register”(Finished.

Click “Modify” on the left side, you can be modify any information of product(Click “Modify”(Finished.

Select “Product” or “Model” on the bottom(Search information of the registered products.

# 4. Backup and restore

The new version increased the extrapolated "Backup and Recovery", "clients" and "product" Backup / Recovery can be achieved separately, Users can upgrade of Product Database, which is no need to change the customer information database. Backup customers and products for the preservation of important information users provide convenient.

### 4-1 Backup

Click “Backup”(Select “Customers Information” or “Product information”(Click  & select the Path of file(Click “ Start”(end

### 4-2 Restore

Restore is simulate “Backup”.

# 5. Registration Search

### 5-1 Customer information

Click “Registration Search” and enter “Customer information”, as below:

5-1-1 New customer register

Click “Register”(enter “the menu of register” as below:

You can capture the customer’s picture by USB camera or Click “Open” to pickup customer’s picture from image folder. Then you must fill in the information on the “ID”, “Name”, “Sex”, “Birth” and other space.(Click “register” on the bottom right corner(Finished.

Click “ok”(return “Customer information”

Click “Next”( enter Main menu.

### 5-2 Non-Member Measure

Click “Non-Member Measure”(enter other Manu for Non-VIP customer(Select “Sex”(input “Birth”(OK!(enter main menu.

# 6. Main Manu

You can enter Main Manu after finishing “Option” and “Product Register”.

### 6-1 Moisture

You can use precision Moisture meter, like DM-R1 from Panasonic, to test the  skin of Moisture. Click T position of the sample face(test moisture of customer’s face(read “digit” on the Moisture meter(input “digit” on the T zone(click “analysis” ( Color piling chart below shows the results.

Same above, Click U position of the sample face(test moisture of customer’s face(read “digit” on the Moisture meter(input “digit” on the U zone(click “analysis” ( Color piling chart below shows the results.

Advances products will be showed on the bottom. The Chart about relation of age and moisture will be display on the top right side. Click “next”(Sebum.

### 6-2 Sebum

5-2-1 Sebum test by simply way

Click and select the T (U) position of sample face(Click “video” (more inf. See the 8-1)(pick up customer’s skin by USB Camera(Click “Capture”(Double click the capture picture(the skin will be display on the main image( Click “Analysis”(ok!

6-2-2 Sebum test by the special oil test cotton

Using the way of 5-2-1 is simply and useful, but it is not accuracy and is good repeat consistency. Sebum test by the special oil test cotton can be got the good result with the high-accuracy, low error and better repeat consistency, but it is not simply operation with high cost.

6-2-3 Compare

Click “compare” on the bottom middle site, you can compare one skin with other skin with different position or different time, also you can draw line, outlines, mark and so on, see as below:

6-2-4 3D

Click “3D”(the similar 3-dimensional skin will be display on the screen(press and move the left key of mouse, you can see the skin of different positions.(Click “F3” got full screen display.

Click “Next” go to 6-3.

### 6-3 Pore

Click and select the T (U) position of sample face(Click “video”(pick up customer’s skin by USB Camera(Click “Capture”(Double click the capture picture(the skin will be display on the main image(go to 5-3-2 and 5-3-3

6-3-1 Zoom in

Click (get yellow square (see as below)(move the yellow square to some place by the left key of mouse(the yellow square may be zoom in full screen.

6-3-2 Line

Click (keep to press the left key of the mouse(move from one point to another point(release the left key of the mouse(got one line with digit.

6-3-3 Circle

Click three points on the outline of area(got the circle cover the area and display digit automatically(see as below.

Click “Analysis”( got the result(Click “next”(go to 5-4

### 6-4 Keratin

Click and select the T (U) position of sample face(Click “video”(pick up customer’s skin by USB Camera(Click “Capture”(Double click the capture picture(the skin will be display on the main image(Click “Analysis”(the result of Keratin, see as below.

The red, yellow and green lamp on the top right corner will be lighted after analysis and tell you the sub-health level of skin automatically.

Click “Next”(go to 5-5

### 6-5 Surface

Click and select the T (U) position of sample face(Click “video”(pick up customer’s skin by USB Camera(Click “Capture”(Double click the capture picture(the skin will be display on the main image(Click “Analysis”(the result of Surface, see as below.

Bad Surface as above and better surface as below

Click “Next”(go to 5-6

### 6-6 Pigmentation

Click and select the T (U) position of sample face(Click “video”(pick up customer’s skin by USB Camera(Click “Capture”(Double click the capture picture(the skin will be display on the main image(Click “Analysis”(the result of Pigmentation, see as below.

Bad Pigmentation as above and better pigmentation as below

Click “Next”(go to 7.

# 7. Client report

Enter read the result of Client report and printout report after finished 6 tests as above.

Click “Product” on the bottom right side of the report( see the match products

### 7-1 products

Return the report after Click “Close”

### 7-2 Printout report

Click “Print” on the bottom right side( two reports can be printout.

You can input some information inside the space of Pore, Keratin, Skinsurface, Pigmentation and Memo

# 8. FQA

### 8-1 How do you know the installation of USB camera is normal?

  - The Skin Camera is similar USB Camera, just the lens and lighting system is different USB camera. So the process of installation is same with normal USB camera. You can check the installation: my computer(hardware(images device(Camera. See left:

### 8-2 The images does not appear on the screen, how to fix?

Move the mouse to main images(Click left button of mouse(Select “Preview +OV519”(OK!

www.dental-camera.com