UV CTCP NEGATIVE PLATE (UV CTnP) TDS

PLATE GAUGES

Standard: 0.15/0.3/0.4mm

COATING-EXPOSURE

Coating colour : Light green

The color is light blue after exposure

Colour change after exposure: high

Contrast after developer: high

Day light sensitivity-UV: it is recommended to work under safety yellow light of low UV radiation.

Spectral sensitivity: 400-450nm. With peak sensitivity at 410nm.

Usable on platesetters with inter mal drum or flat bed.

Screen reproduction: 1%-99% at 200 l.p.i.

Resolution: up to 3200dpi and stochastic(FM)screen 20 microns.

DEVELOPMET

Use developer Kodak 956 or Phoenix. Negative developer.

Kodak 956: Water =1:1.5, Water =1:2, Water =1:2.5, Three kinds of ratio can be.

Phoenix Negative developer.: Water =1:1

Developer temperature:   23°C±1°C.; Fahrenheit:73.4±1.8

Development time:       30±5 seconds i immersion.

Replenishment:          use developer Kodak 956 or PHOENIX-900 as a replenisher.

Replenishment rate:       60ml/㎡

Antioxidant stand by ON   30ml/h.

Antioxidant stand by OFF   30ml/h

When using machine imaging, imaging of the brush should be removed to prevent damage to the image area.

PHOENIX developer is designed for has expired Negative PS Plate preparation of the developing solution

Using PHOENIX developer, can already expired Negative PS Plate resume printing function.

DELETION

Use EAST TOP deletion pens with wide, medium and fine point.

Apply over the area to be corrected and leave for 20-30 seconds.remove by washing with abundant quantities fo water.

Recommended conductivity range: 800-1.500 microsiemens.

Note the results obtained may vary depending if the conditions of use are outside of our recommended values.

| Type: | Negative CTnP plate | Note |
| --- | --- | --- |
| Spectral sensitivity: | 405nm |  |
| Exposure energy: | 90-110mj/cm2 |  |
| Developing time: | 30-40 seconds |  |
| Developing Conditions： | Pure Developer: Water =1:1, Fahrenheit:73.4±1.8 Centigrade:23±1 | Take off the brush when develop in the machine. |
| Resolution: | 1-99%at200l.p.i. |  |
| Run-length: | 200,000-300,000 | (Varies with its printing conditions and imaging content ) |
| CTCP Machine MATTCHED | BasysPrint；Luscher；Cron；PolyTech |  |
| Energy | ≥90mw | Make adjustment according to the speed of machine |
| Drum Speed | ≥700rpm | Make adjustment according to the energy of machine |
| Safelight: | Yellow light |  |

NOTE:

There might be light yellow on the plate after developing. Some suggestions are recommended as follows:

- Please continue to use it without worrying.

- Disappearing quickly: Put it the UV-light to make it disappear quickly.

- Obtained by developing the right image after the UV light in any secondary exposure, printing capabilities can be extended by 50%.

Anhui Phoenix Plate Technology Co., Ltd

Tel: 0086-551-6331111   Fax: 0086-551-6333700

Website:  http://www.phoenix-psplate.com