PSP TO HDMI CONVERTER

User Manual

I. Introduction

When you connect PSP to TV directly, you can only get partial display on the middle area of the TV screen, while with LKV8000, you achieve full-screen display. It not only converts Component Video and Audio R/L of PSP to HDMI, but up-scales PSP output resolution 480P to HDMI 720P, and display in full screen on HDTV. If you want to play PSP at home and on big-screen and high-definition TV to gain wonderful visual enjoyment, LKV8000 is what you can not do without!

II. Features

-1xPSP input, include PSP video and audio.

-1X HDMI output, 1xAudio

-HDMI output: 720P@60Hz

-Compatible with all kinds of HDMI displays

-HDMI 1.3 and HDCP compliant

-Power supply: DC5V/1A

III. Operation Controls and Functions

PSP IN: Connect PSP video and audio in

- PSP IN: Connect PSP video and audio in

- POWER: Connect DC5V/1A power adapter. When connect power adapter, LED lights.

- UDIO OUT: Audio output either integrated with HDMI or output via 3.5mm audio enable connection to sound box and ear phone.

- HDMI OUT: Connect HDTV or any other HDMI displays

IV. Specification of Keys

‘ZOOM’ Key: Enter game picture, press ‘ZOOM’ key on PSP cable, and the picture will switch to full-screen display; press it once again, return to normal display.

V.Connection Image

VI. Settings When PSP Connected to HDMI LCD:

- Settings of PSP When Connected to LCD

Method 1. On main menu, move direction key ‘←’ to select ‘Settings’, move ‘↑’ and ‘↓’ to select ‘Connected Display Settings’, click ‘×’ key enter submenu, move ‘↑’ and ‘↓’key to select ‘switch video output’, and press ‘×’ key, PSP screen turns into black. PSP is switched to the mode of output to LCD successfully.

Method 2. Start PSP, press ‘’ and hold on till  displays on PSP screen, PSP is switched to the mode of output to LCD successfully.

- Settings of PSP Connecting to TV

Enter submenu of ‘Connected Display Settings’ by referring to Method 1, select ‘TV Type’ and press ‘X’, move ‘↑’ and ‘↓’key to select ’16:9’ or ‘4:3’ according to your TV type. Then select ‘Component/D-Terminal…’, press ‘X’, and select ‘Progressive’. (When connect PSP via LKV8000 to TV, here you need to select ‘Progressive’ to get normal display.)

VII. Package and Accessories:

| Item | Qty | Remark |
| --- | --- | --- |
| LKV8000 | 1pcs |  |
| Audio Cable | 1pcs |  |
| 5V/1A Power Adapter | 1pcs |  |
| HDMI Cable | 1pcs |  |
| User Manual | 1pcs |  |