54W Cornbulb

<1>  Dimension and available socket

The size of the product with E39/E40 lamp holder:φ93*283mm

The size of the product with E26/E27 lamp holder:φ93*268mm

<2>Specification

| Model Number | SL-Cornbulb-008D | Warranty Time | 5years |
| --- | --- | --- | --- |
| Led Source | SMD5630 |  |  |
| Led Quantity | 162PCS |  |  |
| Power | 54W |  |  |
| Luminous | 5400lm±50lm |  |  |
| harmonic distortion | <12% |  |  |
| Color Temperature | Warm white | Pure white | Cool white |
|  | 2800-3200K | 4000-4500K | 6000-6500K |
| CRI | 80 |  |  |
| Input Voltage | AC 100-277V 50-60 Hz |  |
| Dimmable | No |  |  |
| Operating Temp | -40°C～50°C |  |  |
| Power Factor | >0.92 |  |  |
| Beam Angle | 360° |  |  |
| Lamp Base | E26 E27 | E39 E40 |  |
| Material | Extruded aluminum heat sink |  |
| Lift Span | 50,000hours |  |  |
| Warranty | 5years |  |  |
| Applications | Indoor lighting |  |  |
| Package | White box/customized, |  |

More packing info, also refer to the following Item No.5

| Eco-Friendly |  |
| --- | --- |
| ◘ Efficient design that greatly reduces energy usage |
| ◘ RoHs compliant(Free of mercury and lead) construction |
| ◘ Produces no ultraviolet radiation(UV) |
| Design |  |
| ◘ Thick aluminum housing for superior heat dissipation |
| ◘ Utilizes high luminosity SMD LED Chips |
| ◘ Compatible with a standard E26 E27 E39 E40 socket |

Operation

◘Instant turn on time(no flickering)

◘Glare free and even light distribution

◘ LED life is unaffected by frequency of use

Reliability

◘ Long operating life of over 50,000hours

◘ Lasts up to 10 times longer than filament lamps

◘ No wear and tear components unlike standard

fluorescent lighting

<3>Luminous emittance

<4> How to select the starlight cornbulb ?

<5>. Package:

| Parameter | Value | Unit | Parameter | Value | Unit |
| --- | --- | --- | --- | --- | --- |
| Single package size | L300*W100*H100/pc | mm | Single carton size | L480W370H380/Carton | mm |
| Net Weight | 1.2 | Kg/PCS | Gross Weight | 1.35 | Kg/PCS |
| QTY/Carton | 12 | PCS/carton | Total Weight | 16.5 | Kg/carton |

Note: The above weight not including the weight of wooden stand.

<6>. Installation project

<7> Notes:

1.Before the installation, please make sure the working voltage on the installed location is consistent with the product.

2.When installing, please confirm the lamp base of the installed corn light is compatible with its lamp

holder.

3.Please turn off the power supply before installing to prevent electric shock.

4.This product does not have dimming function, please do not use dimmer.

5.This product has no waterproof function, it is forbidden to directly put it into water to use.

6.If products do not need to be used in a long time, please store them in a cool, dry and clean environment;

7.When the product emerges non-artificial damage, please do not dismantle and repair it privately, you should send it back to the original company for technical analysis and maintenance;

8.The parameters in this specification will change comply with the upgrading of products ,after changing, there is no further notice, please forgive the inconvenience.