T8 LED Ｕ-Tube

E.T.8 series  2*570mm-18W   Internal Driver

Dimension and available socket

Specification

| Model Number | T8 U-Tube | Warranty Time | 5years |
| --- | --- | --- | --- |
| Led Source | SMD2835 |  |  |
| Led Quantity | 96PCS |  |  |
| Power and dimension | 18W | 2*570mm*26mm | Width 170mm |
| Luminous | 1850-2050LM |  |  |
| Harmonic Distortion | <15% |  |  |
| Color Temperature | Warm white | Pure white | Cool white |
|  | 2800-3200K | 4000-4500K | 6000-6500K |
| CRI | 80 |  |  |
| Input Voltage | AC 85-265V or 100-277V 50-60 Hz |  |
| Dimmable | No |  |  |
| Operating Temp | -20°C～45°C |  |  |
| Power Factor | >0.96 |  |  |
| Beam Angle | 180° |  |  |
| Lamp Base | G13 |  |  |
| Material | Extruded aluminum heat sink |  |
| Lift Span | 50,000hours |  |  |
| Warranty | 5years |  |  |
| Applications | Indoor lighting |  |  |
| Package | White box/customized |  |
| Product Weight(kg) | 0.45/pc |  |  |
| Carton Size(cm) | 650*260* 260(L * W * H)/Carton |  |
| Qty/Ctn | 6pcs |  |  |
| Gross Weight(Kg) | 6.5kg |  |  |

Selections for  More T8Tube

| Eco-Friendly |  |
| --- | --- |
| ◘ Efficient design that greatly reduces energy usage |
| ◘ RoHs compliant(Free of mercury and lead) construction |
| ◘ Produces no ultraviolet radiation(UV) |
| Design |  |
| ◘ Thick aluminum housing for superior heat dissipation |
| ◘ Utilizes high luminosity SMD LED Chips |
| ◘ Compatible with a standard G13 , |

Operation

◘Instant turn on time(no flickering)

◘Glare free and even light distribution

◘ LED life is unaffected by frequency of use

Reliability

◘ Long operating life of over 50,000hours

◘ Lasts up to 10 times longer than filament lamps

◘ No wear and tear components unlike standard

fluorescent lighting

◘UL,CUL,DLC certificate ◘E39/E40 lamp base ◘Warm/Natural/Cool/Cold White◘360 degree lighting, High CRI◘IP64 Rating ◘Big heat sink, double SUNON fans ◘Can be with frosted cover ◘Internal driver, input voltage AC100-277V◘No UV or IR in the beam ◘Easy to install and operate ◘Energy saving, long service life ◘Light is soft and uniform, safe to eyes ◘Instant start, No flickering, No humming ◘Green and eco-friendly without mercury, application widely used in supermarket, warehouse, garage, home office, hotel, hospital, school, street, garden etc.

Luminous emittance

Package info

12pcs/Carton

Carton size is 650mm*260*260mm

Gross weight  6.5kg/Carton

Projects