LED  Panel Light (Waterproof)

SPECIFICATION

PRODUCT：LED Waterproof Panel Light

Model    ：SL-PL004N

1 Basic information

1.1Features

- Water-proof  Luminaire

- PB Free

- CE & ROHS Erp, LM79 Compatible

- LED TYPE：SMD 4014

- CRI：≥80

- Optional CCT：3000K / 4000K / 5000K / 6000K

- Light Angle：120°

- Insulation：CLASSⅡ

- Ingress Protection：IP65

- Working environment：10~80%RH，-20℃~50℃

- Emitting Dimension： 540*540mm

1.2Electrical-Optical Characteristics

| Model | Watts. | LED | Light Eff | Lumen | Power Supply Info. |
| --- | --- | --- | --- | --- | --- |
|  |  | PCS | lm/W | lm | Input | Output | PF | Eff. |
| SL-PL004N | 36 | 360 | 90 | 3240 | 220-240V | 36VDC | 0.9A | 0.96 | 97% |

※Notes：the parameter is based on white color with CCT 4000K/5000K/6000K， light efficiency and luminous will be lower for warm white color with CCT 3000K, +/-10% deviation for parameter of electricity and light can be accepted

2.Installation Instructions

2.1Replace the plaster false ceiling

Flush-mounted installation method

This is the most popular installation for the panel, remove the

False ceiling and replace it with the panel

2.2Suspended to the ceiling

2.3Mounted on the ceiling or the wall ,Surface-mounted method

3.The wiring diagram

4.The Electrical-optical Test Reference

※Notes：This Test report is based on a certain Part Number LED Panel Light

5.The IES test report

※Notes：This AAI Figure is based on a certain Part Number LED Panel Light. Different power consume, CCT and CRI will affect the flux out, Eavg and Emax. For more detail information, please contact our sales.

6. Packing instruction:

Size of inner carton：67*62*3.5CM         Size of master carton：70*75*25CM

G.W of inner carton：4.5KG              G.W of master carton：25KG

Packing quantity：5PCS/mater carton

| 7. Application: municipal lighting、bank lighting、gymnasium lighting、airport、cinema、bus station、Public lighting； hotel、super market、 convenience store、 bar、coffee shop、bathroom、teahouse； Apply to advertisement, fair, stage. Can be used in outdoor. IP65 8. Caution: Turn off all connected power before installation Can’t be soaked in the water for long time. IP is 65 Normal, the standard product is Non-dimmable. For dimmable, please see other instruction information. Any queries, please. call or add whatsapp 86 135 1065 4911 Eco-Friendly |  |
| --- | --- |
| ◘ Efficient design that greatly reduces energy usage |
| ◘ RoHs compliant(Free of mercury and lead) construction |
| ◘ Produces no ultraviolet radiation(UV) |
| Design |  |
| ◘ Thick aluminum housing for superior heat dissipation |
| ◘ Utilizes high luminosity SMD LED Chips |
| ◘ Compatible with a standard 595mm*595mm,600mm*600mm or 603mm*603mm |

Operation

◘Instant turn on time(no flickering)

◘Glare free and even light distribution

◘ LED life is unaffected by frequency of use

Reliability

◘ Long operating life of over 50,000hours

◘ Lasts up to 10 times longer than filament lamps

◘ No wear and tear components unlike standard

fluorescent lighting

◘UL,CUL,DLC certificate ◘Warm/Natural/Cool/Cold White◘360 degree lighting, High CRI◘IP68 Rating ◘Big heat sink, double SUNON fans ◘Can be with frosted cover ◘Internal driver, input voltage AC100-277V◘No UV or IR in the beam ◘Easy to install and operate ◘Energy saving, long service life ◘Light is soft and uniform, safe to eyes ◘Instant start, No flickering, No humming ◘Green and eco-friendly without mercury, application widely used in supermarket, warehouse, garage, home office, hotel, hospital, school, etc.

# Text boxes

ⅲ. push the panel to the frame and it will be clipped and fixed

ⅱ. Screw the 4 clips to the panel

ⅰ. Fix the frame to the ceiling or wall with screws